## Slide 1: Connected Home Council (CHC) Webinar Tuesday, November 26, 2019, 12 NOON – 1:30 PM (ET)
Chair: Roy Perry (Alarm.com, Inc.)
Vice-Chair: Obiorah Ike (ABB, Inc.)
Vice-Chair: Danny Sran (TELUS)

## Slide 2: 1. Agenda Greg Walker (CABA)
1. Agenda
2. Call to Order, Welcome, Introductions, about the CHC
3. Administrative
“Holistic Sustainability and Energy Management: Through the Lens of the Honda Smart Home” (30 min)
    - Michael Koenig (American Honda Motor Co., Inc)
5. Research Update
6. White Paper Sub-Committee Update
7. New Business
8. Announcements
9. Adjournment

## Slide 3: 2. Call to Order, Welcome, Introductions, About the CHC Roy Perry (Alarm.com, Inc.)
Established in 2004, the CABA Connected Home Council initiates and reviews projects that relate to connected home and multiple dwelling unit technologies and applications. The Council also examines industry opportunities that can accelerate the adoption of new technologies, consumer electronics and broadband services within the burgeoning connected home market.
Past CHC Chair
Jay McLellan
VP, Energy Management, Controls and Automation Leviton Manufacturing Co., Inc.
CHC Chair
Roy Perry
VP Ecosystem Alliances
Alarm.com
www.caba.org/chc
CHC Vice-Chair
Obiorah Ike
Product Marketing Manager
ABB Inc.
CHC Vice-Chair
Danny Sran
Mgr. Construction - New Growth Markets TELUS

## Slide 4: 3. Administrative Roy Perry (Alarm.com, Inc.)
3.1 Motion to approve past CHC Minutes:
www.caba.org/chc
September 26, 2019

## Slide 5: 4. “Holistic Sustainability and Energy Management” Greg Walker (CABA)
Holistic Sustainability and Energy Management: Through the Lens of the Honda Smart Home
Michael Koenig
American Honda Motor Co., Inc
Project Leader, Honda Smart Home U.S.

## Slide 6
Michael Koenig
American Honda Motor Co., Inc
Project Leader, Honda Smart Home U.S.
Holistic Sustainability and Energy Management
Through the Lens of the Honda Smart Home

## Slide 7
Honda? The Car Company?

## Slide 8
Striving to be a Company That Society Wants to Exist
“Honda puts climate change and energy at the top of the list of global environmental issues that it needs to address.”
- 2013 Honda Annual Environmental Report

## Slide 9
Honda Smart Home US Vision
The Basics…
1944 square feet single family home (181m2)
Occupant uses the Home and Fit EV vehicle
HSHus is a living laboratory to demonstrate a vision for zero-carbon living and mobility
Zero Net Energy including transportation
Some Background:
California set a 2020 goal for all new residential construction to be Zero Net Energy
Q: How can we make zero-net-energy homes with EVs actually play nicely with the electric grid? AND do it while respecting all facets of sustainability?

## Slide 10
Health
Water
Waste
Energy
Materials
Holistic
Sustainability
Facets of Sustainable Construction

## Slide 11
Where
UC Davis “West Village” community… Zero Net Energy target for the entire village (apartments and future homes)
January 1: Winter - 30’s ~ 50’s, sometimes rainy
July 1: Summer - Hot, desert climate

## Slide 12
Start With The Basics of Orientation and Envelope…
  9.25” Walls + Triple Pane Windows
  Tight envelope
  Optimized Orientation and Overhangs
Summer
Winter
Winter

## Slide 13
Integrated System: Heating, Cooling, Hot Water, Ventilation

## Slide 14
Integrated System: Heating, Cooling, Hot Water, Ventilation
Radiant Heating and Cooling
Single Heat Pump provides Heating, Cooling, and Hot Water
Large diameter boreholes for heat exhangers

## Slide 15
Integrated System: Heating, Cooling, Hot Water, Ventilation
Desuperheater (free hot water… 15 year payback) 23% of hot-water energy
Drain Heat Recovery (free warm water… 40 year payback) 11% of hot-water energy
Where Did the Hot Water Come From (2016)
Figure credit:
Frontier Energy

## Slide 16
Large Diameter Borehole Experiment (2’ x 20’)
Drilling is fast and cheap, but how effective are the heat exchangers?

## Slide 17
Total = 8 Boreholes:
  4 - Wetted by Graywater
  4 - Dry Soil
Large Diameter Borehole Experiment (2’ x 20’)
Answer:
Dry: About 0.20 tons each
Wet: About 0.25 tons each

## Slide 18
Radiant Panels Over Insulation (Mstr Bdrm)

## Slide 19
Radiant Cooling
Post-Tensioning Tendon
Insulation Mat
Hydronic Tubing
+ Higher Set Points yet equal comfort
+ Low pumping energy
- Long time delays
- Cold floors in summer
- Dew Point Control can be challenging

## Slide 20
Vent Cooling… Try 1: Open Clerestories and Pressurize

## Slide 21
Vent Cooling… Try 2: Depressurize with n=5 Bath Fans

## Slide 22
Vent Cooling… Try 3: Start Over With Data
Optimize Energy, Pressure, Noise:
  Whole House Fan
  Exhaust Fans
AND integrated with 62.2 Ventilation
Figure Credit: Frontier Energy

## Slide 23
LED Lighting: Man Max, Machine Min
Lighting Goals:
  Daylighting First
  Comfortable, High Quality
  Energy Efficient
  Healthy

## Slide 24
LED Lighting: Man Max, Machine Min
Everything should just work automatically in the background…
But over-riding is easy with a keypad in every room…
Because fiddling with a control pad is a hassle
1
2
3
But what about when you go to bed?? How does it know when to ignore motion?
Ans: We added a “Sleep” button

## Slide 25
LED Lighting, Circadian Design:
Most Fixtures
= 2700K
Main Array
= Adjustable

## Slide 26
Amber Night Lights
Kitchen and Bath
Hall and Stairs

## Slide 27
Mind the Standby Loads
44% Less Than Average New Construction*
* But controls in general is a killer with 2013 tech.

## Slide 28
Home Control using the Smart Home App

## Slide 29
Energy Management System Details
Hardware:
9.5 kW Solar PV array
10 kW bi-directional inverter
10 kW bi-directional DC charger
10 kWh* Lithium battery
DC Microgrid

## Slide 30
Energy Management System Details
Note: We will publish a report on how to better predict times of low-carbon grid electricity in CA
DC Microgrid
Hardware:
9.5 kW Solar PV array
10 kW bi-directional inverter
10 kW bi-directional DC charger
10 kWh* Lithium battery
Response Examples:
If total house current > 100A
 Discharge battery
To a Demand Response Request
 Discharge car (to net zero P)
In case of solar power fluctuation
 Smooth output using battery
In case of grid voltage fluctuation
 Charge/Discharge battery
 Make hot water (if available)

## Slide 31
Water Savings
Compact Plumbing Design
 Very short hot water runs
Low flow fixtures and dual-flush toilets
Xeriscaped landscape with graywater irrigation

## Slide 32
HSHus used 50% natural ash material
Post-Tensioning reduces concrete volume
Exposed Concrete = No Additional Flooring material
Every pound of cement releases about one pound of carbon dioxide during its manufacture !
Factoid
Sustainable Raw Materials

## Slide 33
All lumber, trim AND furniture is third-party certified for sustainable forestry
Cork, Denim, Cellulose Insulation
Sustainable Raw Materials

## Slide 34
Made in USA
FSC certified
No Formaldehyde
No Chemical Fire Retardants
Sustainable Furniture (examples)

## Slide 35
Indoor Air Quality: Keep The House Dry First…
Rainscreen (air gap) behind siding
Proper grading with swales to direct rainwater to the rain garden

## Slide 36
Automatic humidity sensing
Plus a manual fan control
We track the airflow out of the house:
  Bath fans, Central vac, Range hood
 Then run fans if more air is required
Fresh Air

## Slide 37
Hopefully Some of That Was Interesting.
Now Let’s Move the Ball Down the Field.

## Slide 38
All of Our Drawings and Specs are on the Website…

## Slide 39
Data Loggers
Individual water flows
Data Monitoring…
239 Channels Published @ 1-min resolution
Temperatures, Power, …

## Slide 40
Data Examples
Solar Irradiance (max available solar power)
Actual DC solar power decreases as temperature rises
Refrigerator cycles
Fan stages for night cooling

## Slide 41
Ours is Public Because It’s A Hassle To Do It Yourself!

## Slide 42
www.HondaSmartHome.com
Michael_Koenig@ahm.honda.com

## Slide 43: 4. “Holistic Sustainability and Energy Management” Greg Walker (CABA)
Questions?
Michael Koenig
American Honda Motor Co., Inc
Project Leader, Honda Smart Home U.S.

## Slide 44: 5. Research Update Obiorah Ike (ABB, Inc)
www.caba.org/research
5.1 “Smart Home as a Service” 2019 CHC Landmark Research

## Slide 45: 5. Research Update Greg Walker (CABA)
5.2 2020 CHC Landmark Research Topic?

## Slide 46: 6. White Paper Sub-Committee Update Ken Wacks (Ken Wacks Associates)
6.1 Recently Completed: None

## Slide 47: 6. White Paper Sub-Committee Update Ken Wacks (Ken Wacks Associates)
6.2 In Progress:
“Power over Ethernet (PoE) & Digital Electricity (DE) in Commercial and Multiple Dwelling Residential Buildings”
Somfy Systems, Inc. (Chair)
Contemporary Controls Systems, Inc.
LumenCache, Inc.
National Electrical Manufacturers Association (NEMA)
Public Services and Procurement Canada
Renesas Electronics America Inc.
Southwire Company, LLC
UL LLC

## Slide 48: 6. White Paper Sub-Committee Update Ken Wacks (Ken Wacks Associates)
6.2 In Progress:
“The Ethics of AI and the IoT Connected Home”
ArcoLogix LLC (Chair)
Enbridge Gas Inc.
George Brown College
Hydro One Networks Inc.
Site 1001, Inc.
Sustainable Resources Management Inc.
Syska Hennessy Group, Inc.
Telecommunications Industry Association (TIA)

## Slide 49: 6. White Paper Sub-Committee Update Ken Wacks (Ken Wacks Associates)
6.2 In Progress:
“Human Centric Lighting: Non-Energy Benefits of Lighting and its Smart Controls”
Human Centric Lighting Society (Chair)
ArcoLogix LLC
Control4
National Electrical Manufacturers Association
Syska Hennessy
UL LLC

## Slide 50: 6. White Paper Sub-Committee Update Ken Wacks (Ken Wacks Associates)
6.2 In Progress:
“The Evolution of Integrating LiFi Technology into Smart Lighting and Control Systems for the Intelligent Building”
Wharton County Junior College (Chair)
Acuity Brands, Inc.
ArcoLogix LLC
Control4
National Electrical Manufacturers Association
Telecommunications Industry Association (TIA)

## Slide 51: 6. White Paper Sub-Committee Update Ken Wacks (Ken Wacks Associates)
All proposals and previously completed CHC White Papers can be downloaded at:
www.caba.org/whitepapers

## Slide 52: 7. New Business Roy Perry (Alarm.com)
7.1 Other new CHC business?

## Slide 53: 8. Announcements Greg Walker (CABA)
CEDIA Expo, Sept 10-14, Denver, CO
Greenbuild, Nov 19-20, Atlanta, GA
Smart Home Summit, Nov 19-20, San Francisco, CA
8.1 Past Event Overview:
8.2 Upcoming events:
CABA AGM, Dec 5, via Webinar
CES International 2020, Jan 7-10, Las Vegas, NV
The NAHB International Builders' Show (IBS), Jan 21-23, Las Vegas, NV
The Kitchen & Bath Industry Show (KBIS), Jan 21-23, Las Vegas, NV

## Slide 54: 9. Adjournment Roy Perry (Alarm.com)
Continental Automated Buildings Association (CABA) caba@caba.org www.CABA.org
www.caba.org/chc
Connect to what’s next™
Next CHC Meeting: Late Jan / Early Feb 2019